9 Network over-subscription ON NODEJS 'NODE-BIDDER'

Network over-subscription on the node-bidders occurs when ever more network connections are made to the RTB system to handle increasing bid requests. This is more than simply load balancing. Fully understanding the performance characteristics allows you to determine how much hardware you need to reach your required volumes, and as result, you can determine the cost of a single bid.

To fully understand the performance issue a math model of a typical RTB system will show those areas of the design that limit the volume of bids per RTB process. With the model, three separate causes of poor node-bidder performance are identified. Acting in concert these three factors have had a devastating effect on node-bidder performance.

The first factor affecting performance, especially win ratios, is the bids/second count. Bids/second in the RTB is not linear in behavior. Handling 1000 bids a second in Nodejs for example, is not 1000 bids placed end to end within 1 second. Experimental research has shown it is 500 or so concurrent connections in the node-bidder are doing 1-3 bids per second each. In fact, it is possible to obtain higher bids/second in the system and yet have a win ratio of 0%. It is not how many bids/second the node-bidder can do that matters; instead it is the number of concurrent bids you can do in a second that are less than 100ms in length.

A large component of bid time is the number of concurrent connections allowed by the RTB. If connections are unconstrained, experience has shown the bids/second will go up (for a while), but the win ratio will approach 0%. The behavior of increasing bid times as concurrent connections increase over a 1 second range is best approximated by a geometric growth function. The more you process, the longer the time to bid will be for all subsequent bids.

The second factor affecting performance is processing so-called ‘wide’ opem campaigns. Each campaign in the original node-bidder requires execution of a group of 'if' statements to check all the possible combinations setting forth bid criteria. The sooner a campaign doesn’t match, the fewer resources are used to respond to the request. The more ‘wide’ open a campaign, the more resources that particular request will use because it processes through all the if statements in the campaign.

The third factor affecting performance is the number of campaigns in the system. Because in this node-bidder, processing multiple campaigns requires looping through the same campaign code, once for every campaign on every bid request; processing 10 campaigns per bid dramatically increases (by up to 10 times) processing for a single campaign. The time it takes to process N campaigns is based on how many campaigns there are, and how wide open the campaigns are.

The second and third factors are best modeled as an integral over the ‘wideness’ of a campaign multiplied by the amount of time to bid required to process on a single bid request.

9.1 Performance Model
The model of this section presents the following equation of bid performance 'K':

The bid cost components (in processor resources) of the three factors affecting performance, described above are analyzed in detail in the following sections.
## 9.2 Geometric Growth Cost of Concurrent Connections
Geometric growth is defined by the equation . K is the amount of time it takes to process a single bid at a single connection. The variable r is the percentage increase each successive connection costs, amortized over the total maximum number of connections within 1000ms.
## Value of K
The value of K, the time needed to process a bid is

2b is the time it takes to make 2 REDIS calls on a bid. m/500 is the time it takes a single bid to participate in the bulk insert into the mongo collections used for accounting purposes. The node-bidder never reads from mongo. Experiments with the current RTB systems shows this time to execute the mongo write to be in the noise range.

Harder to wrap your head around is . This is the amount of time it takes to process a single bid request in the face of multiple campaigns with different degrees of openness. The integral is taken varying from 0 campaigns to the max number, defined by c. The function p[c] is simply the value of the probability (openness) of a particular campaign, indexed by c. This integral could be approximated by the average of the probabilities of openness. This is a crude approximation because the range of p is small, and the standard deviation around the mean will likely be relatively large.

9.3 Characteristics of Performance

Examining the model, it is obvious that the exponent x, the number of maximum connections must be managed so that the function’s curve does not accelerate greatly from x-1 to x.
The second component of bid time cost is to realize that , is the time it takes to process c campaigns, and it is multiplied by bid times. Further increasing the bid time is, the more wide open campaigns are, the more contribute to the value of the integral. Campaign processing is serial over the time to make a bid. This is a major source of processing overhead in the nodejs bidder..

9.4 Recommendations
Unconstrained, the node-bidder will perform worse than if constrained. This is due to the geometric growth issue. The maximum value of the exponent x cannot be determined unless a requirement is levied on the system for the number of bids/second required.

Additionally, another requirement must be levied for the nominal time for a bid (and that is less than 125ms). The value of the exponent of x could be reduced by adding additional processors to reduce the ‘pressure’ x on the performance. This requires further analysis of the economics involved in adding processors to achieve deterministic bid rates. This of course affects the cost of bids.

Finally, the equation of node-bidder performance shows that 1000 bids a second maximum turns into 100 bids second maximum with 10 wide open campaigns. No amount of load balancing or processor speeds will make these relative numbers better.

In order to increase the number of bids/second with many wide open campaigns, these campaigns must be processed in parallel. Replacing the serial campaign processing time with simply the largest time to process the ‘widest open’ campaign will greatly increase performance. In such a decoupled system, the performance of a 1 campaign system vs. a 10 campaign system will not be that different. The current activities finding the theoretical maximums for a bidding system should be continued; this will bound the problem.

Additionally, based on the numbers derived from the current testing, requirements need to be levied for the required bids/second with the largest number of campaigns at an average bid time. You need to know what the requirements are in order to build a system that can reach those numbers.

Finally, there is no infinite amount of bids/second on any single computer, or even a bunch of computers. No matter how many instances you field, the average bids/second over all instances will not change much (but cost per bid might increase at some point of diminishing return).